The Presentoire file format

# Generality
Every file needed for a presentoire document must be stored in a single zip file.
It contains for instance pictures, transition classes...
Its main file is a content.xml file, describing the document.

There are three transition possibilities :
- transitions embedded in Presentoire
- transitions provided as a .class file in the presentoire document
- transitions scripted in the presentoire XML file.
When a transition name is solved, the first check is for .class files, then for scripted transitions and finally for embedded transitions.
There are three embedded transitions : rotation, scale and transparency.

The colors are handled using an HTML-like syntax. A few basic colors are defined (red, blue, green, black and white), and you can specify arbitrary colors using #RRGGBBAA (hexadecimal values).

# The content.xml file
This file is the main part of a presentoire document. It contains the entire document, and binds together the other files of the zip file.

Its main root is a document node, with no attribute.
This node can contain two different nodes.

## Transitions
A transition node allows the creation of ScriptTransition objects in the presentation. Other transitions don't need any transition node.
It has two attributes : id (the name of the transition) and language (the name of the scripting language used for this transition, as recognized by the Java6 scripting engine).
Its content is the script. It's better to encapsulate it into a CDATA (but not mandatory).

A script transition requires two functions : before and after. These two functions will be called before and after removing the current slide from the mainComponent. They accept three arguments : the mainComponent (the presentoire window), the slideContainer (the component3D containing the slide) and nextSlide (the Component3D containing the next slide).

## Slides
A slide node has one (currently unused) attribute : id, the name of the slide. Later, it'll be used to jump between various slides using buttons or other elements.
It contains elements showed on the screen.
Currently, there are three elements available :
- img element. It has three attributes : the width and height of the picture on the screen, and src, the filename containing the picture. It has no content.
- text element. It has two attributes : the maximal width and the height of the text to display on the screen. Another optionnal attribute : the color. Its content is the text to display.
- ul element. It has the same attributes as the text element, but its content is only li nodes, containing the text to display.

There are some common attributes for each element :
x, y and z : the position of the element on the slide.